## Slide 1: Router Configuration and Static Routing CS F303
Dr. Pranav M. Pawar

## Slide 2
Packet Tracer is a program used to illustrate how computer networks work.
Packet Tracer has two different views
  Logical Workspace
  Physical Workspace
Packet Tracer also has two modes of operation
  Realtime Mode
  Simulation Mode
Packet Tracer

## Slide 3
Topology

## Slide 4
Drag and drop the required components from the Packet Tracer component toolbox
Create Network
Component toolbox

## Slide 5
Assign addressed to Connections
Device | Connected from | Connected to | IP Address
PC0 | FastEthernet 0 | Switch0 FastEthernet 0/1 | 10.0.0.2
PC1 | FastEthernet 0 | Switch0 FastEthernet 1/1 | 10.0.0.3
Router0 (Gateway) | Switch0 FastEthernet 2/1 | Router0’s FastEthernet 0/1 | 10.0.0.1
Router0 | Serial 2/0 | Router1’s Serial 2/0 | 192.168.0.253
Router1 | Serial 2/0 | Router0’s Serial 2/0 | 192.168.0.254
Router1 (Gateway) | Switch1 FastEthernet 2/1 | Router1’s FastEthernet 0/1 | 20.0.0.1
PC2 | FastEthernet 0 | Switch1 FastEthernet 0/1 | 20.0.0.2
PC3 | FastEthernet 0 | Switch1 FastEthernet 1/1 | 20.0.0.3
IP Address and Default Mask

## Slide 6
Assign IP address to PC0.
  Step 1: Click on PC0, we will get following window.
Assign IP Address PC (1)

## Slide 7
Assign IP address to PC0.
  Step 2: Click on IP configuration and set the IP address, subnet mask and gateway address.
Assign IP address to PC1, PC2, and PC3 in same way.
Assign IP Address PC (2)

## Slide 8
Step1: Double click Router0 and click CLI and press Enter key to access the command prompt of Router0.
Press N in Continue with configuration dialog? [yes/no]:
Configuring Router 0 (1)

## Slide 9
Step 2: Use following commands to configure Router 0, FastEthernet 0/0 interface.
Configuring Router (2)

## Slide 10
Step 2: Use following commands to configure Router 0, Serial 2/0 interface.
Router#configure terminal
Router(config)#interface Serial2/0
Router(config-if)#ip address 192.168.0.253 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#exit
Router#
Configuring Router 0 (2)

## Slide 11
In same way, Configure Serial 2/0 and FastEthernet 0/0 interface.
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#interface FastEthernet0/0
Router(config-if)#ip address 20.0.0.1 255.0.0.0
Router(config-if)#exit
Router(config)#interface FastEthernet0/0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial2/0
Router(config-if)#ip address 192.168.0.254 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#exit
Router#
Configuring Router 1

## Slide 12
For Router 0: Instructs router that when you receive a packet for 20.0.0.0 network give it to 192.168.0.254.
Configure Routing (1)

## Slide 13
For Router 1: Instructs router that when you receive a packet for 10.0.0.0 network give it to 192.168.0.253.
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#ip route 10.0.0.0 255.0.0.0 192.168.0.253
Router(config)#exit
Router#
Configure Routing (2)

## Slide 14
Ping and tracert from PC1 to PC3
Communication from PC1 to PC3

## Slide 15
IPv4 Address
Classes of IPv4 Address
Appendix (1)

## Slide 16
Netid and hostid
Appendix (2)

## Slide 17
Default Mask
Appendix (3)

## Slide 18
Finding a network address using the default mask
Example:
Appendix (4)

## Slide 19
Thank You!