## Slide 1: Dynamic Routing CS F303
Dr. Pranav M. Pawar

## Slide 2
Network Topology

## Slide 3
Assign IP address to PC0 and PC1
Assign IP Address PC
PC0 | 
IP Address | 10.0.0.2
Subnet Mask | 255.0.0.0
Default Gateway | 10.0.0.1
PC1 | 
IP Address | 20.0.0.2
Subnet Mask | 255.0.0.0
Default Gateway | 20.0.0.1

## Slide 4
Configure Fa 0/0, Se 2/0, and Se 3/0 interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#interface FastEthernet0/0
Router(config-if)#ip address 10.0.0.1 255.0.0.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial2/0
Router(config-if)#ip address 192.168.0.252 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial3/0
Router(config-if)#ip address 193.167.0.219 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)# exit
Router(config)#
Configuring Router 0

## Slide 5
Configure Se 2/0 and Se 3/0
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#interface Serial2/0
Router(config-if)#ip address 192.168.0.253 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial3/0
Router(config-if)#ip address 194.16.0.20 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)# exit
Router(config)#
Configuring Router 1

## Slide 6
Configure Fa 0/0, Se 2/0, and Se 3/0 interfaces
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#interface FastEthernet0/0
Router(config-if)#ip address 20.0.0.1 255.0.0.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial2/0
Router(config-if)#ip address 193.167.0.218 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface Serial3/0
Router(config-if)#ip address 194.16.0.21 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)# exit
Router(config)#
Configuring Router 2

## Slide 7
For Router 0
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router rip
Router(config-router)#network 10.0.0.0
Router(config-router)#network 192.168.0.0
Router(config-router)#network 193.167.0.0
Configure dynamic routing

## Slide 8
For Router 1
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router rip
Router(config-router)#network 192.168.0.0
Router(config-router)#network 194.16.0.0
Configure dynamic routing

## Slide 9
For Router 2
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router rip
Router(config-router)#network 20.0.0.0
Router(config-router)#network 193.167.0.0
Router(config-router)#network 194.16.0.0
Configure dynamic routing

## Slide 10
Ping and tracert from PC1 to PC0 and vice versa
Testing of Scenario

## Slide 11
Remove link between Router 0 and Router 2.
Remove Link Router 0-2

## Slide 12
Ping and tracert from PC1 to PC0 and vice versa.
Testing of Scenario

## Slide 13
Simulate the dynamic routing by considering following network scenario.
Ping and tracert from PC0 to PC1,PC2,PC3 and vice versa.
Down the link between Router 0 to Router 2, and observe the difference between tracert outcome from PC0 to PC1.
Practice Scenario

## Slide 14
Router>enable
Router#show ip route
Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
C 10.0.0.0/8 is directly connected, FastEthernet0/0
R 20.0.0.0/8 [120/1] via 193.167.0.218, 00:00:21, Serial3/0
C 192.168.0.0/24 is directly connected, Serial2/0
C 193.167.0.0/24 is directly connected, Serial3/0
R 194.16.0.0/24 [120/1] via 192.168.0.253, 00:00:02, Serial2/0
[120/1] via 193.167.0.218, 00:00:21, Serial3/0
Check routing table entries on each Router

## Slide 15
Thank You!