## Slide 1: Subneting CS F303
Dr. Pranav M. Pawar

## Slide 2
Design a subnet for IP address 192.168.10.0/25
Problem Statements

## Slide 3
Given IP Address: 192.168.10.0 / 25 (Class C)
Subnet mask should consist of 25 1’s as IP address is with /25.
Subnet Mask:
  11111111.11111111.11111111.10000000
  255.255.255.128
No of Subnets:
  No of subnets are depends on number of extra 1s in default subnet mask.
  In current example,
    No of extra 1s in subnet mask than default mask: 1
    Therefore, no of subnets = 21 = 2 subnets
No of host per subnets:
  No of host per subjects depends on number of 0s in subnet mask.
  In current example,
    No of 0s in subnet mask = 7
    Therefore, no of host per subnets = 27 = 128
Subnetting Example (1)

## Slide 4
Valid subnets blocks are,
  192.168.10.0 to 192.168.10.127
  192.168.10.128 to 192.168.10.255
Valid host addresses in each subnets are,
  Subnet1:
    First host address: 192.168.10.1
    Last host address: 192.168.10.126
  Subnet 2:
    First host address: 192.168.10.129
    Last host address: 192.168.10.254
Other addresses in each subnet
  Subnet 1:
    Subnet (Network) address: 192.168.10.0
    Broadcast address: 192.168.10.127
  Subnet 2:
    Subnet (Network) address: 192.168.10.128
    Broadcast address: 192.168.10.255
Subnetting Example (1)

## Slide 5
Subnetting Scenario

## Slide 6
Set the IP address for host and gateway

## Slide 7
Design a subnet for network with IP address 193.175.12.0/26.
Practice Scenario

## Slide 8
Thank You!